FS-1562 Channel  Programming

The FS-1526 can store up to 200 user channels, numbered to 200.

PROGRAMMING

# Procedure

- While pressing and holding down the RCL key , turn the power on.

- Select the system channel  9999 by operating the FREQ/CH encoder.

- Press the RCL,1,5,6,2 and ENT keys in this order.

- Select the system channdl 9998 with the FREQ/CH encoder.

- Press the RCL,0 and ENT keys to enable channel programming.

- Select an RX channel to program,by operating the FREQ/CH encoder.

Display changes as follows when the FREQ/CH encoder is operated.

Channel No.

9999    [1*R]     [1*T]    ****    [200*R]

9998    *************     9900    [200*T]

Channel No.

- Select emission mode with the MODE key.

- To enter a RX frequency , press the RCL key and enter a frequency with the numeral keys , then press the ENT key.

- Select a TX channel of the same channel as RX with the FREQ/CH encoder.

- Enter a TX frequency as follows.

## Simplex

Press the ENT key . The same frequency entered at step 8 is stored.

### Duplex

Press the RCL key,enter a frequency with the numerial keys,then press ENT key.

- To program another channde,repeat steps 6 to 10.

- Set the system channel 9998 to “1”(User channel memory : disable).

- Turn the power off to store channels programmed.

#### TO ERASE AN USER CHANNEL

- Select an RX channel to erase with the FREQ/CH encoder.

- Press the RCL,0,ENT keys in this order.

- Potate the FREQ/CH encoder clockwise by one step to select a TX channel of the same channel as RX.

- Press the RCL,0,ENT keys in this order.

To erase another user channel,repeat 1 to 4.

FS-1562用户频道编程方法

  - 存储用户频道

    - 按住RCL，打开电源。

    - 转动FREQ/CH，选择9999频道。

    - 依次按RCL，1，5，6，2和ENT键。

    - 转动FREQ/CH，选择9998频道。

    - 按RCL，0和ENT键，打开频道编程功能。

    - 转动FREQ/CH，选择一个要编程的接收频道。

转动FREQ/CH，显示变化如下：

Channel No.

9999    [1*R]     [1*T]    ****    [200*R]

9998    *************     9900    [200*T]

频道号

代表接收

    - 按MODE选择工作方式。

    - 按RCL，“数字键”和ENT输入接收频率。

    - 顺时针转动FREQ/CH一步，使上图中“R”变成“T”而保持频道号不变。

    - 输入发射频率方法如下：

同频：

按ENT，将发射频率设成与接收频率相同。

异频：

按RCL，“数字”健和ENT，输入发射频率。

    - 重复6至10编程其它频道。

    - 转动FREQ/CH选择9998频道，按RCL，1，ENT关闭频道编程功能。

    - 关闭电源，存贮已编程频道。

  - 清除用户频道

    - 转动FREQ/CH，选择要清除的接收频道。

    - 依次接RCL，0，ENT键。

    - 顺时针转动FREQ/CH一步，选择发射频道（与接收频道）。

    - 依次按RCL，0，ENT健。

重复1至4清除其它用户频道。

烟台天晟电子科技有限公司(TEL:0535-6844936)

FS-1562日常通讯操作步骤

- 向右转动POWER钮开机，并将音量调到合适位置。

- 将GAIN钮右旋至2/3以上位置（否则会影响接收灵敏度）。

- 按RCL键，再按数字键输入频道数，按ENT。

- 按TX TUNE使显示“TUNE OK”，（非常重要，否则影响

发射效果）；如出现“TUNE ERROR”请不要通讯，要检查天线或请专业人员检修。

- 按话筒上PTT开关讲话，松开PTT开关接收对方的声音（对

方在讲话时，千万不要按PTT开关）。

- 向左转动POWER钮关机。

烟台天晟电子科技有限公司(TEL:0535-6844936)

# Text boxes

1

R              0.00

MODE

J3E

1

R              0.00

MODE

J3E